## Slide 1: Wearable Electronics 3 Hour Summer Camp – Grade 6-8 Day 1

## Slide 2: What are Wearable Electronics?
Our bodies are our primary interface for the world!
Interactive systems that live on the body can be upfront, intimate, literally on your face.
They can sit close to your skin, in your clothing and sometimes might feel like part of you!

## Slide 3: What do people think about Wearable Electronics?
In a survey of 5000 adults in the US (a year back) people were interested
in various wearables as shown here.

## Slide 4: Anatomy of a sample Wearable device
Bluetooth Low Energy
MOST IMPORTANT PART of a Wearable
Update App on phone

## Slide 5: What are Microcontrollers?
The simplest computer processor used as the “brain” of a system.
Depending on the taste of the manufacturer, a bit of memory, a few A/D converters, timers, input/output lines etc. are added
All that is placed in some of the standard packages.
A simple software able to control it all and which everyone can easily learn about has been developed.
A microcontroller is a self-contained system with peripherals, memory and a processor that can be used as an embedded system.

## Slide 6: What are Microcontrollers?
Arduino is an open source computer hardware and software company, project, and user community that designs and manufactures single-board microcontrollers and microcontroller kits for building digital devices and interactive objects that can sense and control objects in the physical world.
Circuit Playground from Adafruit features an ATmega32u4 micro-processor. It also is round and has alligator-clip pads around it. You can power it from USB, a AAA battery pack, or Lipoly (for advanced users). Program your code into it, then take it on the go.

## Slide 7: What is inside a Microcontroller?
A microcontroller chip or board typically has:
  Central processing unit(CPU)
  Random Access Memory)(RAM)
  Read Only Memory(ROM)
  Input/output ports
  Timers and Counters
  Interrupt Controls
  Analog to digital converters
  Digital analog converters
  Serial interfacing ports
  Oscillatory circuits

## Slide 8: Introducing Circuit Playground
Circuit Playground is the name of the little round electronic circuit board that you are going to use as a tool to investigate and explore programming & electronics. Think of it as like a Swiss Army Knife or multi-tool for learning electronics as an art form! It is an all-in-one board so you can jump in quickly and do a whole lotta projects (It can slice, it can dice, it has lots of blinky LEDs!)

## Slide 9: Introducing Circuit Playground

## Slide 10: Introducing Circuit Playground

## Slide 11: Introducing Circuit Playground
10 x mini NeoPixels, each one can display any rainbow color
1 x Motion sensor (LIS3DH triple-axis accelerometer with tap detection, free-fall detection)
1 x Temperature sensor (thermistor)
1 x Light sensor (phototransistor)
1 x Sound sensor (MEMS microphone)
1 x Mini speaker (magnetic buzzer)
2 x Push buttons, left and right
1 x Slide switch
8 x alligator-clip friendly input/output pins Includes I2C, UART, and 4 pins that can do analog inputs/PWM output
All 8 pads can act as capacitive touch inputs
Green "ON" LED so you know its powered
Red "#13" LED for basic blinking
Reset button

## Slide 12: Introducing Circuit Playground
GPIO + Capacitive Touch Pads
Neo-Pixels

## Slide 13: Introducing Circuit Playground
Push Buttons
Slide switch
SWITCHES

## Slide 14: Introducing Circuit Playground
Temperature Sensor
SENSORS
Light Sensor
This sensor is connect to analog pin #A5 and will read between 0 and 1023 with higher values corresponding to higher light levels. A reading of about 300 is common for most indoor light levels.
Calculate the temperature based on the analog voltage on analog pin #A0

## Slide 15: Introducing Circuit Playground
Microphone
AUDIO
Speaker
Make your circuit playground sing with the built in buzzer. This is a miniature magnetic speaker connected to digital pin #5 with a transistor driver. You can use PWM at varying frequencies to make basic tones.
You can read the analog voltage corresponding to the audio on analog pin #A4 (Raw analog audio waveform! When it's silent there will be a reading of ~330 and when loud the audio will read between 0 and 800 or so.

## Slide 16: Introducing Circuit Playground
ACCELEROMETER
The 3-axis XYZ accelerometer is in the dead center of the board and you can use it to detect tilt, gravity, motion, as well as 'tap' and 'double tap' strikes on the board. The LIS3DH is connected to the hardware SPI pins (to leave the I2C pins free) and has the CS pin on digital pin #8 and an optional interrupt output on digital pin #7

## Slide 17: Introducing Circuit Playground

## Slide 18: 10 minutes break

## Slide 19: Project Time – Blinky Circuit!
These pixels are controlled by a single data pin, #17. Unlike non-smart RGB LEDs, you can set the color and a little chip inside the LED will handle the PWM for you.
Since they are controlled in a chain, you will need to tell the Circuit Playground's NeoPixel code which one you want to set the color for. Each NeoPixel is numbered, starting with #0 at the top left and going counter clockwise till you reach #9

## Slide 20: Project Time – Blinky Circuit!
CircuitPlayground.setPixelColor (n, red, green, blue)
Where n is between 0 and 9 and indicates which LED you are setting. red/green/blue vary between 0 (off) and 255 (full on)
You can quickly turn all the LEDs off with CircuitPlayground.clearPixels()
CircuitPlayground.setBrightness(b) where b varies from 0 (no LEDs will ever light) to 255 (incredibly bright!)
SET COLOR
CLEAR COLORS
SET BRIGHTNESS

## Slide 21: Code
#include <Adafruit_CircuitPlayground.h> // Change these to set speed (lower is faster) #define FLASH_RATE 250 #define SPIN_RATE 100 // Change these to be whatever color you want // Use color picker to come up with hex values #define FLASH_COLOR 0xFF0000 #define SPIN_COLOR 0xFF0000 /////////////////////////////////////////////////////////////////////////////// bool buttonsPressed() { return CircuitPlayground.leftButton() | CircuitPlayground.rightButton(); } /////////////////////////////////////////////////////////////////////////////// void flasher() { while (!buttonsPressed()) { // Turn on all the pixels to FLASH_COLOR for (int pixel=0; pixel<10; pixel++) { CircuitPlayground.setPixelColor(pixel, FLASH_COLOR); } // Leave them on for a little bit delay(FLASH_RATE); // Turn off all the NeoPixels CircuitPlayground.clearPixels(); // Leave them off for a little bit delay(FLASH_RATE); } }

## Slide 22: Code
/////////////////////////////////////////////////////////////////////////////// void spinner() { // Can be any two pixels int pixel1 = 0; int pixel2 = 5; while (!buttonsPressed()) { // Turn off all the NeoPixels CircuitPlayground.clearPixels(); // Turn on two pixels to SPIN_COLOR CircuitPlayground.setPixelColor(pixel1, SPIN_COLOR); CircuitPlayground.setPixelColor(pixel2, SPIN_COLOR); // Increment pixels to move them around the board pixel1 = pixel1 + 1; pixel2 = pixel2 + 1; // Check pixel values if (pixel1 > 9) pixel1 = 0; if (pixel2 > 9) pixel2 = 0; // Wait a little bit so we don't spin too fast delay(SPIN_RATE); } } /////////////////////////////////////////////////////////////////////////////// void setup() { CircuitPlayground.begin(); // Make it bright! CircuitPlayground.setBrightness(255); } /////////////////////////////////////////////////////////////////////////////// void loop() { flasher(); delay(250); spinner(); delay(250); }

## Slide 23: Q&A

## Slide 24
What are Wearable Electronics?
What are Microcontrollers? Where are they used?
Introduction to Circuit Playground, pins, sensors, switches and more…
PROJECT TIME: Blinky/Flash/Spin NeoPixel Circuit
1. https://learn.adafruit.com/circuit-playground-lesson-number-0?view=all#library-reference